## Slide 1: VLSI Implementation of DENLMS Adaptive Filter for Biomedical Applications
Low-Power & High-Speed ECG Noise Removal Architecture
Authors C. Venkatesan, T. Thamaraimanalan, R. Latha
Mohammad Ali Sakib
ID No : 220137
Reg.:1011979 Dept. of CSE Pabna University of Science and Technology

## Slide 2: Contents :
Core Problem and Context
Context
Challenge
Solution Needed
Problem Motivation
Non-stationary nature of ECG noise
Limitations of traditional FIR/IIR filters
Adaptive Filter Concept
What is an adaptive filter
Why adaptive filtering is required
Limitations of Existing LMS-Based Methods
LMS
ENLMS
DNLMS
Proposed DENLMS Adaptive Filter
Key idea
Delayed error concept
Advantages
Algorithm & VLSI Architecture
DENLMS weight update equation
Pipelined hardware architecture
Implementation & Design Flow
HDL design
Simulation
Synthesis & layout
Results & Performance Analysis
Error comparison
Power, area, and speed comparison
Key Findings
Why DENLMS is better
Suitability for wearable ECG devices
Conclusion
Question And Answer Part

## Slide 3: The Core Problem & Context

## Slide 4: Context
In healthcare, clean Electrocardiogram (ECG) signals are vital for accurate diagnosis. However, these signals are often corrupted by noise during recording and transmission.

## Slide 5: Challenge :
Traditional fixed filters (like FIR/IIR) struggle because ECG noise is non-stationary—its statistics change over time.
Here “non-stationary” means that the statistical properties of the ECG signal or its noise are not constant over time.

## Slide 6: Solution Needed:
We require adaptive filters that can "learn" and adjust to changing noise in real-time.

## Slide 7: PROBLEM MOTIVATION
Why This Work is Needed ?
“ECG signals change over time. Fixed filters cannot adapt. So adaptive filters are required, especially for wearable medical devices.”
ECG signals are non-stationary
Affected by:
White Gaussian noise
Channel noise
Traditional FIR / IIR filters fail
Need:
Adaptive filter
Low Power
High speed hardware

## Slide 8: WHAT IS AN ADAPTIVE FILTER ?
Adaptive Filter Concept :
Self-adjusting digital filter
Minimizes error signal
Updates coefficients automatically
Working Diagram of Adaptive Filter :
Input → Filter → Output
↑
Error

## Slide 9: LIMITATION OF EXISTING LMS (Least Mean Square ) :
Problems
Long critical path
High latency
More power consumption
ENLMS & DNLMS still inefficient

## Slide 10: PROPOSED SOLUTION DENLMS Adaptive Filter ( Delayed Error Normalized LMS )

## Slide 11
Key Idea
Introduce delay element in error path
Use pipelined architecture
Reduce critical path delay
Advantages :
Faster operation
Lower power
Suitable for biomedical VLSI

## Slide 12: VLSI CHIP Architecture :
Standard cells (NAND, NOR, Inverters)
Synthesized using TSMC 130nm
ASIC design flow
“This shows the physical realization of the adaptive filter using standard VLSI cells.”

## Slide 13: DENLMS Algorithm & Implementation Details

## Slide 14
w(n+1)=w(n)+μe(n)x(n)
Problem:
Long critical path
Slow hardware execution
w(n+1)=w(n)+∥x(n)∥2μ​e(n)x(n)
Improvement: Stability Still problem: High power & delay
Normalized LMS (ENLMS)
Conventional LMS Weight Update

## Slide 15: Proposed DENLMS Weight Update
w(n+1)=w(n)+μe(n−m)x(n−m)
Key Modification
Error is delayed by m samples
Enables pipelining
“Here we modify the LMS algorithm by introducing a delay in the error feedback path”.

## Slide 16: Why Delay Helps?
Breaks feedback loop
Reduces critical path
Allows parallel execution
Improves clock speed
Here delay means DENLMS
Proposed Architecture
16-bit pipeline
FIR filter
SUB block for error
Adaptive coefficient update
NOTE : “This is the core contribution of the paper.”

## Slide 17: HDL & IMPLEMENTATION FLOW
Tools Used
Verilog HDL
ModelSim (Simulation)
Xilinx ISE (FPGA)
Synopss DC (ASIC)
RTL Design
(Verilog/VHDL)
Simulation
(Functional)
Synthesis
(Gate Level)
Layout
(Physical)
VLSI Design Flow Diagram
Target FPGA
Virtex-5 XC5LVX330

## Slide 18: SIMULATION RESULTS 
NOTE : “Lower error means better ECG noise removal.”
ENLMS vs DENLMS
DENLMS error is much lower
Stable output with 16-bit precision

## Slide 19: FINAL CHIP LAYOUT
Observation
Area slightly increased
Performance greatly improved

## Slide 20: PERFORMANCE COMPARISON :
Parameter | ENLMS | DNLMS | Proposed DENLMS | Improvement by DENLMS
Total Dynamic Power | 84 mW | 71 mW | 64 mW | 23.8% lower than ENLMS
Cell Leakage Power | 176 µW | 159 µW | 124 µW | 29.5% lower than ENLMS
Total Area (Logic Cells) | ~31.5 K | ~328.6 K | ~335.5 K | 20.4% increase
Slack (Timing Margin) | 0.27 | 0.31 | 0.19 | Lower slack, enables faster clock

## Slide 21
“This is the bar diagram of the previous slide. Its give us a beautiful visualization of the comparison between ENLMS,DNLMS,DENLMS”.

## Slide 22: KEY RESULTS :
Why DENLMS is Better
Low dynamic power
Low leakage power
High speed
ECG suitable
Wearable-friendly

## Slide 23: Some Short Note of This Paper :
Note-2 : Best trade-off between:
Power
Speed
Area
Note-1 : DENLMS outperforms ENLMS & DNLMS
Note-3 : Ideal for biomedical ECG devices

## Slide 24
CONCLUSION :
“This work proves that smart pipelined adaptive filters can save power without sacrificing performance.”

## Slide 25
THANK YOU

## Slide 26
Any Question ?